## Slide 1: Proximity Sensing Cap for the Visually Impaired

## Slide 2: About Good Vision is a precious gift, but unfortunately loss of vision is becoming common these days. Our prototype, Proximity Sensing Cap is built for the aid of visually impaired individuals for navigation and obstacle/surrounding detection.

## Slide 3
Components
The components used for this project are :
Development Board Arduino Uno.
Sensors Ultrasonic Sensors - “HC-SR04” x 3
Others 1. LRA Vibrators x 2
2. Buzzer x 1
3. 9V Battery

## Slide 4: Code #define trigPin1 2 #define echoPin1 3 #define trigPin2 4 #define echoPin2 5 #define trigPin3 6 #define echoPin3 7 #define vibrator1 9 #define vibrator2 11 #define buzzer 13 void setup(){ pinMode(trigPin1, OUTPUT); pinMode(echoPin1, INPUT); pinMode(trigPin2, OUTPUT); pinMode(echoPin2, INPUT); pinMode(trigPin3, OUTPUT); pinMode(echoPin3, INPUT); pinMode(vibrator1, OUTPUT); pinMode(vibrator2, OUTPUT); pinMode(buzzer, OUTPUT); Serial.begin(9600);}

## Slide 5: void loop(){ long duration, distance; digitalWrite(trigPin1, LOW); delayMicroseconds(2); digitalWrite(trigPin1, HIGH); delayMicroseconds(1); digitalWrite(trigPin1, LOW); duration = pulseIn(echoPin1, HIGH); distance = (duration/2) / 29.1; if(distance>=10 && distance < 100){ digitalWrite(buzzer,HIGH); Serial.println(distance);} else if(distance >=100 && distance <150){ digitalWrite(buzzer,HIGH); delay(100); Serial.println(distance); digitalWrite(buzzer,LOW);} else if (distance>=160){ digitalWrite(buzzer,LOW); Serial.println(distance);} delay(200); digitalWrite(trigPin2, LOW); delayMicroseconds(2);

## Slide 6: digitalWrite(trigPin2, HIGH); delayMicroseconds(1); digitalWrite(trigPin2, LOW); duration = pulseIn(echoPin2, HIGH); distance = (duration/2) / 29.1; if (distance < 70){ digitalWrite(vibrator1,HIGH);} else{ digitalWrite(vibrator1,LOW); } delay(200); digitalWrite(trigPin3, LOW); delayMicroseconds(2); digitalWrite(trigPin3, HIGH); delayMicroseconds(2); digitalWrite(trigPin3, LOW); duration = pulseIn(echoPin3, HIGH); distance = (duration/2) / 29.1; if (distance < 70){ digitalWrite(vibrator2,HIGH);} else{ digitalWrite(vibrator2,LOW); } delay(200);}

## Slide 7: Project By : SALONI GOVIL 01FB16ECS333 ROHAN MOHAPATRA 01FB16ECS307 SAKSHAM GOYAL 01FB16ECS332 SAILESH GADDALAY 01FB16ECS331